## Slide 1: Network Operation Check
Notes: [Sources]
- Πρότυπο: A4.M2 Πολυμέσα-Ήχος(2).pptx
[/Sources]

## Slide 2: Network Settings
A.5.M2 | Theory
IP Address
A unique logical address that identifies a device within a network.
Subnet Mask
It determines which part of the IP address identifies the network and which part identifies the device.
Default Gateway
The address of the router that forwards data to other networks.
Notes: [Sources]
- Τετράδιο Εργασιών Πληροφορικής Α΄ Λυκείου, A.5.M2, Δραστηριότητες Εμπέδωσης, σελ. 87–89
- Σημειώσεις Πληροφορικής Α΄ Λυκείου, ενότητα Α.5
[/Sources]

## Slide 3: Subnets
A.5.M2 | Theory
Same Subnet
Two devices on the same subnet can communicate without an intermediate router.
Another Network
When the destination is on another network, the device sends the packets to the default gateway.
Uniqueness
Each active device needs a different IP address on the same network.
Notes: [Sources]
- Τετράδιο Εργασιών Πληροφορικής Α΄ Λυκείου, A.5.M2, Δραστηριότητες Εμπέδωσης, σελ. 87–89
- Σημειώσεις Πληροφορικής Α΄ Λυκείου, ενότητα Α.5
[/Sources]

## Slide 4: DNS
A.5.M2 | Theory
Names and IP Addresses
DNS maps a website name to its corresponding IP address.
DNS Server
The computer queries a DNS server to find the destination address.
nslookup
This command displays information about the mapping between names and IP addresses.
Notes: [Sources]
- Τετράδιο Εργασιών Πληροφορικής Α΄ Λυκείου, A.5.M2, Δραστηριότητες Εμπέδωσης, σελ. 87–89
- Σημειώσεις Πληροφορικής Α΄ Λυκείου, ενότητα Α.5
[/Sources]

## Slide 5: Diagnostic Commands
A.5.M2 | Theory
ipconfig
Displays the IP address, subnet mask and default gateway.
ipconfig /all
Displays additional information, such as the physical address and DNS servers.
ping
Checks whether a destination responds through the network.
tracert
Shows the intermediate routers on the path to the destination.
Notes: [Sources]
- Τετράδιο Εργασιών Πληροφορικής Α΄ Λυκείου, A.5.M2, Δραστηριότητες Εμπέδωσης, σελ. 87–89
- Σημειώσεις Πληροφορικής Α΄ Λυκείου, ενότητα Α.5
[/Sources]

## Slide 6: Connection Speed
A.5.M2 | Theory
Download
The rate at which data travels from the Internet to the device.
Upload
The rate at which data travels from the device to the Internet.
Mbps
A common unit used to measure connection speed.
Notes: [Sources]
- Τετράδιο Εργασιών Πληροφορικής Α΄ Λυκείου, A.5.M2, Δραστηριότητες Εμπέδωσης, σελ. 87–89
- Σημειώσεις Πληροφορικής Α΄ Λυκείου, ενότητα Α.5
[/Sources]

## Slide 7: Troubleshooting
A.5.M2 | Theory
Physical Connection
Check cables, ports, indicator lights and the wireless connection.
Settings
Check the IP address, subnet mask and default gateway.
Tests
Test communication with the router first and then with a remote destination.
Notes: [Sources]
- Τετράδιο Εργασιών Πληροφορικής Α΄ Λυκείου, A.5.M2, Δραστηριότητες Εμπέδωσης, σελ. 87–89
- Σημειώσεις Πληροφορικής Α΄ Λυκείου, ενότητα Α.5
[/Sources]

## Slide 8: Reinforcement Activities
A.5.M2
Questions to Answer
Questions 1–12 in Worksheet A.5.M2.
Notes: [Sources]
- Τετράδιο Εργασιών Πληροφορικής Α΄ Λυκείου, A.5.M2, Δραστηριότητες Εμπέδωσης, σελ. 87–89
- Σημειώσεις Πληροφορικής Α΄ Λυκείου, ενότητα Α.5
[/Sources]